ArduinoGirls
Beginner analog and digital electronics tutorials.
# Schematic Symbols

Symbol	Name	What it Does	Units	Notes
	Power source ; / also known as Vcc	Provides energy (+)	Volts (V)
	Ground ; / also known as Gnd	Provides energy (-)	Volts (V)
	Power source (+ and – terminals)	Provides energy	Volts (V)	The “longer” end of the symbol is positive, the “shorter” negative.
	Capacitor	Stores energy temporarily	Farads (F)	Some capacitors (electrolytic, metallic) are polarized (direction matters!) and are marked as such. Ceramic capacitors are not direction sensitive.
	Light Emitting Diode (LED)	Shines light		Direction matters – the “longer” leg (the “base” of the triangular symbol) is positive
	Potentiometer	Allows to regulate resistance by turning a knob	Ohms ( Ω )	The “center” terminal is what changes “value”. Direction does not matter.
	Resistor	Resists current flow	Ohms ( Ω )	Direction does not matter. Resistor value is color-coded on it with colored stripes.
	(Push) Button	Switches things on and off		Can be sticky (press and it stays on) or not. Direction does not matter.

# Units and Stuff
Name	Unit	What it Is
Voltage	Volt (V)
Current	Ampere (A)
Resistance	Ohm (Ω)
Capacitance	Farad (F)	How much energy is can fit into a capacitor

# LED With A Switch
Shiny!

## Materials
ID	Storage Ref	Notes
R1		Anywhere from 50 … 300 Ω is fine
LED1	CAT 050 or CAT 056 or CAT 044	Any color
BAT	CAT 039	3V CR2450 coin cell
S1	CAT 009 or CAT 010	Any switch

- Why is the resistor needed?
- What happens when we increase or decrease the resistor’s value?
- What happens if the LED is inserted in the wrong direction?

# LED With a Potentiometer

## Materials
ID	Storage Ref	Notes
R1		Anywhere from 50 … 300 Ω is fine
LED1	CAT 050 or CAT 056 or CAT 044	Any color
BAT	CAT 039	3V CR2450 coin cell
R2	CAT 045 + CAT 049

# LED with a Capacitor

## Materials
ID	Storage Ref	Notes
R1		Anywhere from 50 … 300 Ω is fine
LED1	CAT 050 or CAT 056 or CAT 044	Any color
BAT	CAT 039	3V CR2450 coin cell
S1	CAT 009 or CAT 010	Any switch
C1		Polarization (direction) matters!

What happens when we use a larger capacitor?

# Blinking LED (aka Hello World)

## Materials
ID	Storage Ref	Notes
R1		Anywhere from 50 … 300 Ω is fine
LED1	CAT 050 or CAT 056 or CAT 044	Any color

## Spec
Program the Arduino such that it would blink a LED connected to one of the Digital pins (see: blink.ino)
Experiment with with different timings. Write a SOS blinker (see: sos.ino)

# Darkness Warning

## Materials
ID	Storage Ref	Notes
R1		Anywhere from 50 … 300 Ω is fine
LED1	CAT 050 or CAT 056 or CAT 044	Any color
R2
R3	CAT 033	LDR, polarity does not matter

## Spec
Connect a light sensor and a LED with the Arduino. Program the Arduino to warn (by lighting the LED) when it’s getting darker.